Using Correlator
Windowing Functions
For Cheaper Surveys?
A. Marcellin, O. Smirnov,
C. Tasse, G. Foster, J. Jonas

---
Credits

---
Smearing
- A correlator produces visibilities averaged over time/frequency bins
  - ...and we often want to average down further in post-processing, to save space & computing time
- Complex averaging: loss of amplitude
  - off-center sources, long baselines
  - Time- and bandwidth smearing
- For surveys, this imposes a limit on how much you can average (need to retain sensitivity over FoV)
- For VLBI, this imposes tiny FoVs (much smaller than the available primary beam)

---
What Causes Smearing, 1

---
What Causes Smearing, 2
Averaging:
where B is a boxcar (“tophat”) function for the bin. This is a convolution:

---
Averaging ≈ Convolution
Smearing
response
R

---
Windowing Functions
- The smearing response R(l,m) = F-1(B) is unity at 0, decreases radially, but too rapidly initially and not rapidly enough afterwards
- So, why not play with B to optimize smearing response?
  - Replace it with some windowing function W
  - Bread-and-butter filter theory
- The trade-off: increased thermal noise
  - Noise is minimal when sum is unweighted

---
Early Results

---
Oversized Filters?
- Why not use overlapping windows?
- Can we win back some of our noise losses perhaps?

---
Results: Sinc Filter

---
Increasing Integration Time

---
Early Prospects
- We can practically eliminate smearing over a given FoV
- ...and better suppress sources outside the FoV
- ...with little to no increase in noise
- ...while averaging the data down at will:
  - natural limit: spectral resolution
  - natural limit: uv sampling
  - natural limit: calibration
  - but factors of several to orders of magnitude seem within reach

---
Correlator Implications?
- Same input rate
- Output rate reduced by factor of many
- For an overlap factor of N, xN more ops (and registers)