Observing Transients With Low-N, East-West Interferometers
For The Discerning Masochist
O. Smirnov (Rhodes University & SKA SA)

---
Introduction
- Cir X-1 ATCA observations by Mickael Coriat
- 2.1, 5.5, 9 and 33/35 GHz
- Goal: image the jets and
  measure their angle,
  variability with wavelength?

---
Problems
- E-W array, instantaneous
  uv-coverage is a line
- Measurement of structure
  completely degenerate
  w.r.t. intrinsic variability
- Jets are quite close to
  source (given our resolution),
  very delicate detection
- ~6 mJy source “too faint for selfcal?”
- Relying on external calibration....

---
(a) External calibration
Tentative jet detection?

---
(a) External calibration
- Dominated by radial artefacts (tropospheric phase?)
  - Tentative jets detection, but doubtful due to artefacts
- Bright northern source exhibits same artefacts
  - ⇒ direction-independent effect
  - ⇒ selfcal could (?) take care of it
- But, not enough flux for selfcal (~6 mJy)

---
(b) Selfcal/stefcal
- Fortunately, another 6 mJy in northern source
- Can also increase SNR by imposing a slow and smooth variation on the calibration solutions
  - Not possible with legacy software packages
  - ...but doable with “stefcal” in MeqTrees
  - (...and also with Cyril's filter approach)

---
Stefcal Solutions

---
Stefcal Solutions

---
(b) After stefcal
- Radial artefacts gone
  - But so is the tentative jets detection (wasn't real)
- Source position incorrect, not subtracted properly

---
(c) Differential gain on Cir X-1
- Selfcal:
- Differential gain:
  - dE term slowly varying (G fast-varying), takes care of calibration errors towards source (and absorbs intrinsic variability and sky model errors)

---
(c) Differential gain on Cir X-1
- Hint of jets emerging...
- Source position still not quite correct, let's update

---
(d) Updated central source model
- Very compelling jet detection
- Note that jets are suppressed by selfcal and dE's
  - Need to be included in sky model

---
Source Suppression
- Any source not in sky model will be suppressed (by having its flux absorbed into the G and dE solutions)
- How to mitigate:
  - Update sky model to include source
  - Minimize degrees-of-freedom in G and dE
  - For dE, can try an amplitude-only, common-to-all antennas solution ( dEp≡ dE0 )

---
(e) Jets included in model, dEp≡ dE0
12 μJy noise, 96 μJy jet detection

---
Light Curves (?)
- dE solutions absorb intrinsic variability in I and Q
- Proxy for light curves, but degenerate w.r.t. structure

---
Pondering The Process...
1. “A high quality radio map is a lot like a sausage, you might be curious about how it was made, but trust me you really don't want to know.”
   – Jack Hickish, Oxford
Bayesians have full posteriors.
Others have error bars, at least.
We have... plausible maps?
“If the sausage tastes good, it's probably kosh kudu.” – me, Kruger

---
What's The Answer?
- Ideally, each pixel needs an error bar
  - Better yet, an Npix ´ Npix covariance matrix
  - Better yet, full posteriors (science fiction)
- Somewhat out of reach for now
- Short term: Bayesian source fitting?
  - Fit source components, obtain full posteriors
  - “The jets are at position angle θ±σθ”
  - “The measurement is degenerate w.r.t. XYZ...”

---
Conclusions
- Transients on E-W arrays are for masochists
- Nonetheless, with a bit of delicate processing, Cir X-1 jets can be detected reliably
  - ...which only underscores what a dodgy business radio maps really are.
- The future is in
  posteriors?